## Slide 2: Motor imagery
Multisensory-cued
Algorithm (combining)
Sequence motor imagery

## Slide 3
Multisensory-cued -> train -> test (real-time with some algorithm)
  Things to do prepare
    The game
      Consider: color blindness, fixation point
    The data acquisition
      Band-pass 0.5-40, band-stop(notch) at 50Hz
      Re-referencing: Common average or linked-mastoid
      Epoch extraction: how long is the time window post-cue?
      Sampling rate
      downsample>?
      Artifact removal: ICA, NPD(non-parametric directionality)[volume conduction], CAR
    The algorithm
      Feature extraction (CSP
    Performance metrics
      Classification accuracy

## Slide 4: Experimental Design (Setup)
Fixation Cross (Baseline): 2s
Cues: 1s
Motor Imagery: 5s
Inter-trial interval: 2s
Trial per class: 40 trials/class in Rahman et al. 2019; 60 trials/class in Hsu et al. 2022. Total trials: (4 classes × trials/class)
One action per trial (no sequence learning)
Random action but will be balanced
1 trial: 9s
A block: 48 trials: 7.2 mins
After 1 block, short break for 1 mins
One session: 6 blocks
In total: 48x6 = 288 trials
Total time per session: 7.2x6 + 1x6 = 49.2 min
Data collection Session/Calibration 6 blocks
Short game testing (real-time)[optional]

## Slide 5
Is there a difference in the eeg signal in the non-sensory area with single vs multiple sensory cues vs no cues?